## Slide 1
AJ Ribeiro (Space@VT)
ACF Fitting
SuperDARN 2011
A comparison of ACF fitting methods
A.J. Ribeiro (1), P.V. Ponomarenko (2), J. M. Ruohoniemi (1), R.A. Greenwald (1), K. Oksavik (3), J.B.H. Baker (1), L.B.N. Clausen (1)
(1) Bradley Department of Electrical and Computer Engineering, Virginia Tech, Blacksburg, Virginia, USA; (2) Institute of Space and Atmospheric Studies, University of Saskatchewan, Saskatoon, Saskatchewan, Canada; (3) Department of Arctic Geophysics, University Centre in Svalbard, Longyearbyen, Norway
SuperDARN Workshop 2011

## Slide 2
Introduction
AJ Ribeiro (Space@VT)
ACF Fitting
SuperDARN 2011
Introduction
Outline
Background on SuperDARN ACFs
A brief overview of the 3 methods for fitting ACFS
  FITACF
  FITEX2
  LMFIT
Background on the dataset
Results
Conclusions

## Slide 3
SuperDARN ACFs
AJ Ribeiro (Space@VT)
ACF Fitting
SuperDARN 2011
Background
ACFs
Themis -tauscan ACF from 05/18/11 at Goose Bay
Complex autocorrelation functions are calculated fro each range gate from the raw voltages recorded by the receivers
Phase shift between lags (atan(Im/Re)) is fit to determine the Doppler velocity
  This can pose a problem, because for velocities in the hundreds of meters per second, the phase from lag 0 to the last lag changes by more than 2π
Decay of the signal is fit to determine the spectral width and power
  We will focus on a Lorentzian fit
  The magnitude (sqrt(Re^2+Im^2)) is assumed to decay exponentially with time (lag)
  A linear least-squares fit is performed on the log of the magnitudes, the slope is the fitted decay, and the y-intercept is the fitted power

## Slide 4
FITACF
AJ Ribeiro (Space@VT)
ACF Fitting
SuperDARN 2011
Fitting Methods
FITACF
Standard for SuperDARN ACF fitting
Developed by numerous people over the years
Very fast
Phase shifts of the first few lags is used to make a guess at the number of 2π phase skips that occur throughout the entire ACF
  Velocity is fitted with this guess
  For the Lorentzian fit, power and spectral width are determined with a linear least-square fit to the log of the lag magnitudes

## Slide 5
  FITEX2
AJ Ribeiro (Space@VT)
ACF Fitting
SuperDARN 2011
Fitting Methods
FITEX2
FITEX originally developed by Ray Greenwald and Kjellmar Oksavik in order to fit tauscan data
Slower than FITACF
The Lorentzian power and spectral width fits are done the same way as FITACF
Velocity fitting is done differently
  Instead of guessing at the 2π phase skips, it fits the “sawtooth” pattern by comparing the ACF phase variation with 120 model phase variations in 1.5° increments
    This only provided ~25 m/s resolution on resolved velocities
  FITEX2 was developed, which used the best model phase variation as an initial guess, and applied the bisection method to gain arbitrary resolution
  Also was expanded for application to non-tauscan data

## Slide 6
LMFIT
AJ Ribeiro (Space@VT)
ACF Fitting
SuperDARN 2011
Fitting Methods
LMFIT
In 2008, Ponomarenko et al. used the Levenberg-Marquardt method to fit mixed-scatter ACFs
The L-M method is an algorithm that can be used to perform a non-linear least-squares fit
  It is capable of fitting magnitude, decay time, and Doppler frequency of the ACF simultaneously, with no worry of 2π phase skips
  We used the free C library MPFIT to perform the L-M method

## Slide 7
Dataset
AJ Ribeiro (Space@VT)
ACF Fitting
SuperDARN 2011
Dataset
Background
In order to asses the performance of the 3 methods, we need to know what the correct answer actually is
  A simulated dataset was used
    100000 ACFS were generated with NAVE=78 and lag 0 power normalized to 1
    Old pulse sequence: 0,9,12,20,22,26,27
    Velocity in steps of 100 from 50 m/s to 1950 m/s
    Decay time in steps of .01 s from .01 s to .1 s
    500 samples at each step
      Bad lags calculated based on 100 range gates

## Slide 8
Results
AJ Ribeiro (Space@VT)
ACF Fitting
SuperDARN 2011
Results
Results 1
Velocity Error | Mean Error (%) | Median Error (%)
FITACF | 2.42 | 0.475
FITEX2 | 2.14 | 0.495
LMFIT | 1.51 | 0.455
Width Error | Mean Error (%) | Median Error (%)
FITACF | 16.1 | 13.7
FITEX2 | 16.2 | 13.8
LMFIT | 14.9 | 12.7
ACF Error (RMS) | Mean Error | Median Error
FITACF | 0.082 | 0.069
FITEX2 | 0.075 | 0.069
LMFIT | 0.072 | 0.068

## Slide 9
Velocity vs. ACF Error
AJ Ribeiro (Space@VT)
ACF Fitting
SuperDARN 2011
Results
Results 2
For FITEX2 and LMFIT, ACF fitting error does not increase with velocity
For FITACF, velocity error does not seem to increase with velocity, until about 1 km/s, where the error spikes
For all 3, there is an apparent increasing error with lower decay times (increasing spectral width)

## Slide 10
Decay Time vs. ACF Error
AJ Ribeiro (Space@VT)
ACF Fitting
SuperDARN 2011
Results
Results 3
As was implied by the previous slides, ACF error indeed increases with decreasing decay time
LMFIT produces the best results until τd ~ .03 (spectral width ~ 130 m/s)
After this point, LMFIT and FITEX2 produce very similar results
FITACF also produces very similar results, until the velocity becomes sufficiently high (~ 1 km/s)

## Slide 11
Velocity vs. Velocity Error
AJ Ribeiro (Space@VT)
ACF Fitting
SuperDARN 2011
Results
Results 4
Again, error for LMFIT and FITEX2 is not affected by increasing velocity
Again, FITACF is also stable until v > ~ 1 km/s
  Outperforms FITEX2 for v < 1km/s until τd ~ .03
It appears that decreasing decay time lowers the velocity at which FITACF begins having issues
Decreasing decay time increases error for all 3 methods

## Slide 12
Decay Time vs. Decay Time Error
AJ Ribeiro (Space@VT)
ACF Fitting
SuperDARN 2011
Results
Results 5
Yet again, error increases with decreasing decay time
FITACF and FITEX2 are very comparable
  This makes sense, since the fitting method is the same
  LMFIT outperforms the other 2 methods until τd ~ .03
    After this, they all seem to stabilize
  Increasing velocity does not appear to cause an increase in decay time error

## Slide 13
What’s going on?
AJ Ribeiro (Space@VT)
ACF Fitting
SuperDARN 2011
Results
Results 6
In general, LMFIT outperforms both FITEX2 and FITACF, as shown by mean and median errors
  Sometimes, only slightly
FITACF has an added problem at high (> 1 km/s) velocities
If one of the first few lags is bad, it does not get a good guess at the number of 2π phase jumps
If this occurs, FITACF will get a very bad fit for the velocity

## Slide 14
One more look…
AJ Ribeiro (Space@VT)
ACF Fitting
SuperDARN 2011
Results
Results 7
This shows “true” (signed) velocity error
FITEX2 and LMFIT average out to 0 across all errors (no bias)
FITACF also has no bias, until velocity increases above the point where it can’t get a good guess at 2π phase skips
  After this point, it is biased low

## Slide 15
Conclusions
AJ Ribeiro (Space@VT)
ACF Fitting
SuperDARN 2011
Conclusions
FITACF is great for the amount of time it takes
  1 full day of Themis-tauscan data takes ~ 10 seconds to process
  FITACF is the most suitable method for fitting ACFs during runtime at the radars
FITEX2 is capable for fitting velocities without bias and with reasonable errors, but it is slower
  1 full day of Themis-tauscan data takes ~ 15 seconds to process
LMFIT outperforms the other 2 methods across all tests, but is the slowest option
  1 full day of Themis-tauscan data takes ~ 60 seconds to process
  Not suitable for runtime
In an environment when processing time is not a significant concern, LMFIT is the best option for the processing of RAWACF files
  Code also can be optimized to decrease processing time

## Slide 16
Questions?
AJ Ribeiro (Space@VT)
ACF Fitting
SuperDARN 2011
Conclusions

## Slide 17
References
AJ Ribeiro (Space@VT)
ACF Fitting
SuperDARN 2011
References
Ponomarenko, P. V., C. L. Waters, F. W. Menk, (2008), Effects of mixed scatter on SuperDARN convection maps, Ann. Geophys., 26, 1517-1523, doi:10.5194/angeo-26- 1517-2008.