## Slide 1: Investigations of cross-channel interference on a stereo SuperDARN radar
A. McDonald (1), J. Devlin (2).
(1) Department of Physics, La Trobe University, Victoria, Australia
(2) Department of Electronic Engineering, La Trobe University, Victoria, Australia

## Slide 2: Abstract
Interference between channels while operating in two channel 'stereo' mode is investigated for the TIGER Unwin SuperDARN radar. A discretionary mode was run in which channel A cycles sequentially over a number of pre-set frequencies while channel B remains fixed.
It was found that for certain values of the channel A and channel B frequencies and for certain beams, the number of echoes received on the fixed frequency channel B depends strongly on the frequency on channel A at the time. For a stereo radar to be operating properly there should be no such correlation effects between channels.
This cross-channel interference is observed not to depend on ionospheric conditions, only on the particular frequencies used. Spurious channel B echoes resulting from cross-channel interference exhibit low velocities, an absence of low spectral widths and occur at intermediate ranges. Results of a number of tests are presented providing insight into this issue currently under investigation.

## Slide 3: Sequential Frequency Mode
For each 1-minute scan over all 16 beams, channel A is fixed at one of five pre-set frequencies while channel B scans in a synchronous manner at a single fixed frequency.
Channel A cycles through fixed frequencies 9050,10190,12190,14390 and 16350 kHz sequentially for 1 minute each while Channel B is fixed at 10390 kHz.

## Slide 4
We analysed channel B (fixed frequency) echo occurrence with regards to the channel A frequency in operation at the time, to check for cross-channel interference.
Figure 1). Spurious channel B echoes on a number of beams when channel A is 16350 kHz.
No spurious channel B echoes.

## Slide 5
As a reference we calculated the expected value and standard deviation for
randomly binning channel B echoes, into 5 frequency bins.
If there is no correlation between channel B echo occurrence and channel A frequency, the channel B echoes for each beam should be evenly distributed over the 5 channel A frequencies.
This means the 5 occurrence distributions should coincide.
The Problem
In Figure 1), clearly a much greater number of channel B echoes is detected when channel A is scanning at 16350 kHz, particularly on beams 11, 14 and 15.
This effect is not seen all the time, depending critically on the channel B (fixed) frequency chosen, and on the channel A frequency. The details of this frequency dependence is still unclear.

## Slide 6
The effect does not seem to depend on ionospheric conditions.
For the original sequential frequency mode (channel B=10390 kHz and
channel A=[9050,10190,12190,14390,16350]), the same effects are reproduced
on all 20 days analysed over a three-month period, over widely varying
ionospheric conditions.

## Slide 7
The main focus has been on 16350 kHz
The generation of spurious echoes is clearly frequency dependent.
Analysis of interference as channel A frequency approaches 16350 kHz, shows a progressive growth in spurious channel B echoes.

## Slide 8
The effect is not seen on channel A.
In addition, there are no spikes in channel A echo occurrences at the same time and on the same beams as the spurious channel B echoes are occurring.
(in Figure 1 for example)
Running the sequential frequency mode with
channels switched and analysing channel A echo
occurrences (Figure 2) shows no spurious spikes.
No dependence of channel A echo occurrence
on channel B frequencies is observed.
Figure 2.

## Slide 9: Characteristics of spurious channel B echoes
Range
Spectral Width

## Slide 10
Velocity
Excluding velocities < | 100 m/s |

## Slide 11: Frequency bands vs fixed frequencies
In the original mode, the selected frequencies were rigidly fixed,
by-passing the clear frequency search in the radar operating system.
The effect on cross-channel interference of re-instating frequency bands of
non-zero width was also investigated.

## Slide 15
The CUTLASS Pykkvibaer radar is very similar to TIGER Unwin, with close to
identical hardware and software.
In this mode, Milan et. al. use channel A as the fixed frequency and
Channel B for the sequential frequencies.
Data from other Stereo SuperDARN Radars

## Slide 16: Conclusions
The channel B echo count is sometimes unreliable, exhibiting a dependence on the frequency channel A is scanning on.
Channel A echo counts are reliable.
The interference on channel B is a hardware issue. The pulse sequence for a stereo radar is not symmetric between channels, with channel A always leading. A maintenance trip to the radar is planned to perform hardware tests.
The characteristics of the spurious channel B echoes are:
    low velocities, with magnitude < 100 m/s
    an absence of low spectral widths
    intermediate ranges 1000 – 2000 km.
Recommendations
When using stereo modes, routinely check for cross-channel interference.
Use frequency bands with non-zero width of around 500 kHz.